## Slide 1
OSI (Open System Interconnections) (Imp) : It is a network architecture model based on the ISO standards. It is called the OSI model as it deals with connecting the systems that are open for communication with other systems. The OSI model has seven layers. The principles used to arrive at the seven layers can be summarized briefly as below:
  Create a new layer if a different abstraction is needed.
  Each layer should have a well-defined function.
  The function of each layer is chosen based on internationally standardized protocols.
Seven Layers :

## Slide 2
Physical Layer
  It is the lowest layer of the OSI reference model.
  It is used for the transmission of an unstructured raw bit stream over a physical medium.
  Physical layer transmits the data either in the form of electrical/optical or mechanical form.
  The physical layer is mainly used for the physical connection between the devices, and such physical connection can be made by using twisted-pair cable, fibre-optic or wireless transmission media.
DataLink Layer
  It is used for transferring the data from one node to another node.
  It receives the data from the network layer and converts the data into data frames and then attaches the physical address to these frames which are sent to the physical layer.
  It enables the error-free transfer of data from one node to another node.
Functions of Data-link layer:
Frame synchronization: Data-link layer converts the data into frames, and it ensures that the destination must recognize the starting and ending of each frame.
Flow control: Data-link layer controls the data flow within the network.

## Slide 3
Error control: It detects and corrects the error occurred during the transmission from source to destination.
Addressing: Data-link layers attach the physical address with the data frames so that the individual machines can be easily identified.
Link management: Data-link layer manages the initiation, maintenance and termination of the link between the source and destination for the effective exchange of data.
Network Layer
  Network layer converts the logical address into the physical address.
  The routing concept means it determines the best route for the packet to travel from source to the destination.
Functions of network layer :
  Routing: The network layer determines the best route from source to destination. This function is known as routing.
  Logical addressing: The network layer defines the addressing scheme to identify each device uniquely.
  Packetizing: The network layer receives the data from the upper layer and converts the data into packets. This process is known as packetizing.
  Internetworking: The network layer provides the logical connection between the different types of networks for forming a bigger network.
  Fragmentation: It is a process of dividing the packets into fragments..

## Slide 4
4. Transport Layer
  It delivers the message through the network and provides error checking so that no error occurs during the transfer of data.
  It provides two kinds of services:
    Connection-oriented transmission: In this transmission, the receiver sends the acknowledgement to the sender after the packet has been received.
    Connectionless transmission: In this transmission, the receiver does not send the acknowledgement to the sender.
Session Layer
  The main responsibility of the session layer is beginning, maintaining and ending the communication between the devices.
  Session layer also reports the error coming from the upper layers.
  Session layer establishes and maintains the session between the two users.

## Slide 5
6. Presentation Layer
  The presentation layer is also known as a Translation layer as it translates the data from one format to another format.
  At the sender side, this layer translates the data format used by the application layer to the common format and at the receiver side, this layer translates the common format into a format used by the application layer.
Functions of presentation layer:
    Character code translation
    Data conversion
    Data compression
    Data encryption
7. Application Layer
  Application layer enables the user to access the network.
  It is the topmost layer of the OSI reference model.
  Application layer protocols are file transfer protocol, simple mail transfer protocol, domain name system, etc.
  The most widely used application protocol is HTTP(Hypertext transfer protocol ). A user sends the request for the web page using HTTP.

## Slide 6
TCP/IP Reference Model : It is a compressed version of the OSI model with only 4 layers. It was developed by the US Department of Defence (DoD) in the 1860s. The name of this model is based on 2 standard protocols used i.e. TCP (Transmission Control Protocol) and IP (Internet Protocol).
  Link : Decides which links such as serial lines or classic Ethernet must be used to meet the needs of the connectionless internet layer. Ex - Sonet, Ethernet
  Internet : The internet layer is the most important layer which holds the whole architecture together. It delivers the IP packets where they are supposed to be delivered. Ex - IP, ICMP.
  Transport : Its functionality is almost the same as the OSI transport layer. It enables peer entities on the network to carry on a conversation. Ex - TCP, UDP (User Datagram Protocol)
  Application : It contains all the higher-level protocols. Ex - HTTP, SMTP, RTP, DNS.
HTTP and HTTPS :
HTTP is the HyperText Transfer Protocol which defines the set of rules and standards on how the information can be transmitted on the World Wide Web (WWW). It helps the web browsers and web servers for communication. It is a ‘stateless protocol’ where each command is independent with respect to the previous command. HTTP is an application layer protocol built upon the TCP. It uses port 80 by default.
HTTPS is the HyperText Transfer Protocol Secure or Secure HTTP. It is an advanced and secured version of HTTP. On top of HTTP, SSL/TLS protocol is used to provide security. It enables secure transactions by encrypting the communication and also helps identify network servers securely. It uses port 443 by default.

## Slide 7
Important Protocols
A protocol is a set of rules which is used to govern all the aspects of information communication.The main elements of a protocol are:
Syntax: It specifies the structure or format of the data. It also specifies the order in which they are presented.
Semantics: It specifies the meaning of each section of bits.
Timing: Timing specifies two characteristics: When data should be sent and how fast it can be sent.
DHCP: DHCP is the Dynamic Host Configuration Protocol. It is an application layer protocol used to auto-configure devices on IP networks enabling them to use the TCP and UDP-based protocols. The DHCP servers auto-assign the IPs and other network configurations to the devices individually which enables them to communicate over the IP network. It helps to get the subnet mask, IP address and helps to resolve the DNS. It uses port 67 by default.
FTP : FTP is a File Transfer Protocol. It is an application layer protocol used to transfer files and data reliably and efficiently between hosts. It can also be used to download files from remote servers to your computer. It uses port 27 by default.
ICMP : ICMP is the Internet Control Message Protocol. It is a network layer protocol used for error handling. It is mainly used by network devices like routers for diagnosing the network connection issues and crucial for error reporting and testing if the data is reaching the preferred destination in time. It uses port 7 by default.
ARP : ARP is Address Resolution Protocol. It is a network-level protocol used to convert the logical address i.e. IP address to the device's physical address i.e. MAC address. It can also be used to get the MAC address of devices when they are trying to communicate over the local network.
RIP :RIP stands for Routing Information Protocol. It is accessed by the routers to send data from one network to another. RIP is a dynamic protocol which is used to find the best route from source to the destination over a network by using the hop count
algorithm. Routers use this protocol to exchange the network topology information. This protocol can be used by small or medium-sized networks.

## Slide 8
MAC address and IP address (Imp) :
  Both MAC (Media Access Control) Address and IP Address are used to uniquely define a device on the internet. NIC Card’s Manufacturer provides the MAC Address, on the other hand Internet Service Provider provides IP Address.
  The main difference between MAC and IP address is that MAC Address is used to ensure the physical address of a computer. It uniquely identifies the devices on a network. While IP addresses are used to uniquely identify the connection of a network with that device taking part in a network.
Ipconfig and Ifconfig :
  Ipconfig : Internet Protocol Configuration, It is a command used in Microsoft operating systems to view and configure network interfaces
  Ifconfig : Interface Configuration, It is a command used in MAC, Linux, UNIX operating systems to view and configure network interfaces