## Slide 1
Computer Networks
Network : A network is a set of devices that are connected with a physical media link. In a network, two or more nodes are connected by a physical link or two or more networks are connected by one or more nodes. A network is a collection of devices connected to each other to allow the sharing of data.
Network Topology : Network topology specifies the layout of a computer network. It shows how devices and cables are connected to each other.
Types of Network Topology :
  Star :
    Star topology is a network topology in which all the nodes are connected to a single device known as a central device.
    Star topology requires more cable compared to other topologies. Therefore, it is more robust as a failure in one cable will only disconnect a specific computer connected to this cable.
    If the central device is damaged, then the whole network fails.
    Star topology is very easy to install, manage and troubleshoot. It is commonly used in office and home networks.

## Slide 2
Ring :
  Ring topology is a network topology in which nodes are exactly connected to two or more nodes and thus, forming a single continuous path for the transmission.
  It does not need any central server to control the connectivity among the nodes.
  If the single node is damaged, then the whole network fails.
  Ring topology is very rarely used as it is expensive, difficult to install and manage.
  Examples of Ring topology are SONET network, SDH network, etc.

## Slide 3
Bus :
  Bus topology is a network topology in which all the nodes are connected to a single cable known as a central cable or bus.
  It acts as a shared communication medium, i.e., if any device wants to send the data to other devices, then it will send the data over the bus which in turn sends the data to all the attached devices.
  Bus topology is useful for a small number of devices.
  As if the bus is damaged then the whole network fails.

## Slide 4
Mesh :
  Mesh topology is a network topology in which all the nodes are individually connected to other nodes.
  It does not need any central switch or hub to control the connectivity among the nodes.
  Mesh topology is categorized into two parts: Fully connected mesh topology: In this topology, all the nodes are connected to each other. Partially connected mesh topology: In this topology, all the nodes are not connected to each other.
  It is robust as a failure in one cable will only disconnect the specified computer connected to this cable.
  Mesh topology is rarely used as installation and configuration are difficult when connectivity gets more.
  Cabling cost is high as it requires bulk wiring.

## Slide 5
Tree :
  Tree topology is a combination of star and bus topology. It is also known as the expanded star topology.
  In tree topology, all the star networks are connected to a single bus.
  Ethernet protocol is used in this topology.
  In this, the whole network is divided into segments known as star networks which can be easily maintained. If one segment is damaged, there is no effect on other segments.
  Tree topology depends on the "main bus," and if it breaks, then the whole network gets damaged

## Slide 6
Hybrid :
  A hybrid topology is a combination of different topologies to form a resulting topology.
  If star topology is connected with another star topology, then it remains a star topology. If star topology is connected with different topology, then it becomes a Hybrid topology.
  It provides flexibility as it can be implemented in a different network environment.

## Slide 7
Different Types of Networks : (Imp) - Networks can be divided on the basis of area of distribution. For example:
PAN (Personal Area Network): Its range limit is up to 10 meters. It is created for personal use. Generally, personal devices are connected to this network. For example computers, telephones, fax, printers, etc.
LAN (Local Area Network): It is used for a small geographical location like office,
hospital, school, etc.
HAN (House Area Network): It is actually a LAN that is used within a house and used to connect homely devices like personal computers, phones, printers, etc.
CAN (Campus Area Network): It is a connection of devices within a campus area which links to other departments of the organization within the same campus.
MAN (Metropolitan Area Network): It is used to connect the devices which span to large cities like metropolitan cities over a wide geographical area.
WAN (Wide Area Network): It is used over a wide geographical location that may range to connect cities and countries.
GAN (Global Area Network): It uses satellites to connect devices over the global area.

## Slide 8
VPN (Virtual Private Network) : VPN or the Virtual Private Network is a private WAN (Wide Area Network) built on the internet. It allows the creation of a secured tunnel (protected network) between different networks using the internet (public network). By using the VPN, a client can connect to the organization’s network remotely.
Advantages of VPN :
  VPN is used to connect offices in different geographical locations remotely and is cheaper when compared to WAN connections.
  VPN is used for secure transactions and confidential data transfer between multiple offices located in different geographical locations.
  VPN keeps an organization’s information secured against any potential threats or intrusions by using virtualization.
  VPN encrypts the internet traffic and disguises the online identity.

## Slide 9
Types of VPN :
Access VPN: Access VPN is used to provide connectivity to remote mobile users and telecommuters. It serves as an alternative to dial-up connections or ISDN (Integrated Services Digital Network) connections. It is a low-cost solution and provides a wide range of connectivity.
Site-to-Site VPN: A Site-to-Site or Router-to-Router VPN is commonly used in large companies having branches in different locations to connect the network of one office to another in different locations. There are 2 sub-categories as mentioned below:
Intranet VPN: Intranet VPN is useful for connecting remote offices in different geographical locations using shared infrastructure (internet connectivity and servers) with the same accessibility policies as a private WAN (wide area network).
Extranet VPN: Extranet VPN uses shared infrastructure over an intranet, suppliers, customers, partners, and other entities and connects them using dedicated connections.

## Slide 10
IPv4 Address : An IP address is a 32-bit dynamic address of a node in the network. An IPv4 address has 4 octets of 8-bit each with each number with a value up to 255. IPv4 classes are differentiated based on the number of hosts it supports on the network. There are five types of IPv4 classes and are based on the first octet of IP addresses which are classified as Class A, B, C, D, or E.